## Slide 1: Spectrum MRI: Towards Diagnosis of Multi-Radio Interference in the Unlicensed Band

## Slide 2: Introduction
Spectrum Overlap in the 2.4Ghz band
Standards | PHY Characteristics
802.11b | DSSS + BPSK, QPSK, CCK
802.11g | OFDM + BPSK,QPSK,mQAM
Bluetooth | FHSS + GFSK
ZigBee | DSSS + BPSK, QPSK
Others | Cordless Phones, Microwave Ovens, etc.
Specifications of different standards in the 2.4Ghz Band
Increasing density & data rate of radio devices leading to interference limitations.
No means of co-operation and arbitration in the unlicensed spectrum
Is it possible to classify and diagnose multi-radio interference problems by
passive monitoring?

## Slide 3: Common Examples
VoIP over WiFi using a Bluetooth headset
Voice quality degradation due to co-located radios
ZigBee Alarm system co-existent with high rate streaming links
Alarm system messages blocked by WiFi streaming video traffic
Bluetooth links near 802.11b WiFi link
Throughput: 4.92 Mbps
Throughput: 1.92 Mbps
Throughput: 0.42 Mbps
Bluetooth causes a large drop in WiFi throughput

## Slide 4: Interference Basics: Intra WiFi
A
DIFS
Frame
B
Frame
C
D
DIFS
defer
defer
defer
DIFS
Frame
DIFS
Frame
DIFS
Frame
Waiting for free channel
Actual Transmission time
Waiting time for each link increases with addition of new links leading to
throughput drop for every user
Combined throughput of all devices also goes down with increasing number
of links due to increase in collision time

## Slide 5: Interference Basics: WiFi-BT
Bluetooth hops on 79 1Mhz channels, WiFi Bandwidth = 20 Mhz
⇒ Chances of frequency overlap = 20/79 ≈ 25%
Slower WiFi packets occupy more time ⇒ More chances of time overlap

## Slide 6: Interference From Neighbors
Interference Regions of multiple wireless devices operating in a home setting
Interference problem compounds in closely packed neighbourhoods

## Slide 7: Interference Localization
Ideally we would like to locate sources of interference
But indoor localization is a hard problem in itself
  requirement of multiple sensors, training data
  physical dimensions needed for accuracy
  non-uniform transmit power poses additional problem for localization
We take the approach of logical topology discovery when physical topology is hard to find
  system based on user registered devices indexed by their MAC identification

## Slide 8: Project Overview
Network Discovery and Diagnosis Tools
802.11 Probing in Monitor mode
Bluetooth Spectrum sensing
Zigbee Channel Sniffing
Low-cost Spectrum Analyzer
Device side performance logs
Bluetooth Active Sniffing
Network Layer Info from Wired-end
Localization from multiple sensors
Hierarchical Probing
Diagnosis Inference Algorithm
Performance Improvement & QoS Support
Emulation Data from Representative Problem Scenarios
Collection &
Integration
Server
Framework
Control Channel
Direct Configuration Change
Use of Common Channel for Control

## Slide 9
Problem Detection
Exploring what the problem is
Developing tools for data collection
Applying diagnosis algorithms
Intra 802.11 Interference
Inter-radio Interference
  – 802.11-Bluetooth Interference
  – 802.11-ZigBee Interference
  – Bluetooth-ZigBee Interference
Complex Multi-radio Interference
1. Intra 802.11 interference
Topology | Link 2 at 11 Mbps | Link 2 at 1Mbps
11b-11b | 3.76 Mbps | 1.19 Mbps
11g-11b | 25.10 Mbps | 17.60 Mbps
11g-11g | 17.91 Mbps | 9.67 Mbps
Link 1 Throughput for varying Link 2 rates

## Slide 10
Problem Detection
2. Bluetooth – 802.11 interference
Configurations:
802.11b: TCP at 11 Mbps
802.11g: TCP at 24 Mbps
Bluetooth: UDP with 512 Kbps offered load
Distance between 802.11 Rx & Bluetooth Tx: 25cm

## Slide 11
Problem Detection
3. Multi-radio Interference Scenario
Drop in Zigbee throughput: From 83% packet reception to < 2% packet reception

## Slide 12: Developing Tools
Exploring what the problem is
Developing tools for data collection
Applying diagnosis algorithms
Use OML as the underlying framework for data collection
Modify/develop tools which log traces to this framework for different radios
Identify the parameters of interest for each kind of radio
Important and hard topic of synchronization of multiple traces
  - Combine traces from similar monitors
  - Time synchronize traces from disparate monitors
Develop algorithms for adaptive control of the monitors

## Slide 13: Developing Tools: 802.11
1. 802.11 Sniffing (Promiscuous mode)
Separate table for each link seen by each sensor
Another table for recording all the beacons seen by the monitors
Snapshot of a link table from the database

## Slide 14: Developing Tools: Bluetooth
Snapshot of the Bluetooth sniffing information
If the Master BDAddr is known, it is possible to sniff the piconet
But implementation issues due to hardware inaccessibility
Commercial sniffer-FTS4BT ( ~ $10,000 !!) that does this
2. Bluetooth Packet Sniffing

## Slide 15: Developing Tools: Spectrum
3. Spectrum Analysis for Bluetooth
  Scan narrow band spectrum using USRP-GNURadio
  Find high energy 1Mhz bursts in scanned data
  Extract start times of each packet detected
  Estimate no. of piconets by binning the start times which are separated by an integer number of slots

## Slide 16: Developing Tools: Bluetooth
Problem Case: High Powered 802.11 nearby
Solution:
Move to another region in the spectrum (Bluetooth present but Interference absent)
Scan between channels 1 & 6, 6 & 11
802.11b Tx Power: 20dbm (100mW)
Bluetooth Tx Power: 4dbm (2.5mW)
Theoretically possible to detect
with additional processing

## Slide 17: Diagnosis Algorithms
Exploring what the problem is
Developing tools for data collection
Applying diagnosis algorithms
Time Synchronized
Multi-radio Database
Time Synchronized
Drop in 802.11 Rate +
Start of Bluetooth capture
Increased no. of MAC retries +
Traffic in adjacent channel
Loss in periodic ZigBee data +
Detection of video stream
ACK reception at monitor but repetitive retransmissions
Spectrum detection of wide-band interferer like Microwave
Continuous Channel hogging as in DoS attack
Many transmissions on same 802.11 channel
Simplistic Diagnostic Examples

## Slide 18: Diagnosis Algorithms
A more concrete example
No
Interference
With
802.11g
With
Bluetooth
25.2 Mbps
14.4 Mbps
15.4 Mbps
254 % Increase
40.3 %
Increase
With
802.11g
With
Bluetooth
Throughput
No. of MAC
retransmissions
Throughput
Improvement
19.9 Mbps
24.8 Mbps
Change
802.11
Channel
Disable
Autorate
HD Video Example: Demo Recording
Main Link
Interfering Link

## Slide 19: Diagnosis Algorithms
Rule Based Diagnosis
Diagnosis Inference Algorithm
Heuristic Expert System
Multi-radio Sniffing Database
Protocol Specifica-tions
References: [Yan ’09]
[Rayanchu ‘08]

## Slide 20: Some Insights
Possible to parameterize interferences based on observables:

## Slide 21: Some Insights
Current work on characterization of problems vs parameters: filling up the table
 | Packet Error | Channel Occupancy | Round Trip Time | Rate fallback | % MAC Retries | Packet Collision | Spectral Occupancy
Poor signal strength | X | - | X | X | X | - | -
Excessive traffic | X | X | - | - | - | X | -
Adjacent channel interference |  |  |  |  |  |  | 
Hidden node problem |  |  |  |  |  |  | 
Channel hogging by slow link |  |  |  |  |  |  | 
Co-channel Interference |  |  |  |  |  |  | 
Microwave Oven Interference |  |  |  |  |  |  | 
2.4GHz Phone Interference |  |  |  |  |  |  | 
Bluetooth/ZigBee interference |  |  |  |  |  |  | 
Deliberate Jamming |  |  |  |  |  |  | 
Possible
Problems
Diagnostic
Parameters

## Slide 22: Diagnosis Algorithms – Open Issues
Main emphasis of research on this aspect of Diagnosis Inference Algorithms
How to design the expert systems
How to choose parameters to sniff & log in database
How to apply data mining techniques for fault detection
Can we have multi-level hierarchical probing
What things can be done after diagnosis
What if we do have a common shared channel
How to make it feasible (cost, time, complexity)

## Slide 23: References
[Golmie ’03] N. Golmie, N. Chevrollier, and O. Rebala, “Bluetooth and wlan coexistence: Challenges and solutions,” IEEE Wireless Communications Magazine, vol. 10, pp. 22–29, 2003.
[Shin ’07] S. Y. Shin, H. S. Park, S. Choi, and W. H. Kwon, “Packet error rate analysis of zigbee under wlan and bluetooth interferences,” IEEE Trans on Wireless Commun, vol. 6, no. 8, 2007.
[Jing ‘08] X. Jing, et al., “Distributed coordination schemes for multi-radio co-existence in dense spectrum environments: An experimental study on the orbit testbed,” in Proc. of DySPAN 2008, 3rd IEEE Symposium on New Frontiers in Dynamic Spectrum Access Networks, Oct. 2008.
[Gummadi ‘07] R. Gummadi, D. Wetherall, B. Greenstein, and S. Seshan, “Understanding and mitigating the impact of rf interference on 802.11 networks,” in Proc. of Sigcomm07, 2007.
[Bellardo ’03] J. Bellardo and S. Savage, “802.11 Denial-of-Service Attacks: Real Vulnerabilities and Practical Solutions,” Proc. 11th Usenix Security Symp., Usenix Assoc., 2003.
[Stranne ‘06] A. Stranne, O. Edfors, and B.-A. Molin, “Energy-based interference analysis of heterogeneous packet radio networks.” IEEE Trans on Commun., vol. 54, no. 4, 2006.
[Cheng ’07] Y.-C. Cheng, et al., “Automating cross-layer diagnosis of enterprise wireless networks,” in Proc. of Sigcomm07. ACM Press, , pp. 25–36., 2007.
[Sheth ‘06] A. Sheth, et al., “Mojo: a distributed physical layer anomaly detection system for 802.11 wlans,” in Proc. of MobiSys ’06, 2006.
[Yan ’09] B. Yan and G. Chen, “Model-based Fault Diagnosis for IEEE 802.11 Wireless LANs,” in Proc. of MobiQuitous ‘09, Toronto, Canada, July 2009.
[Rayanchu ‘08] S. Rayanchu, et al., “Diagnosing Wireless Packet Losses in 802.11: Separating Collision from Weak Signal”, in Proc. of IEEE Infocom ‘08, 2008.