## Slide 1
VibWrite: Towards Finger-input Authentication on Ubiquitous Surfaces via Physical Vibration
Presenter: Jian Liu
Jian Liu†, Chen Wang†, Yingying Chen†, Nitesh Saxena‡,
†WINLAB, Rutgers University, NJ, USA
‡University of Alabama at Birmingham, AL, USA
DAISY Data Analysis and Information SecuritY Lab
CCS 2017
Dallas, USA
Oct. 31 – Nov. 3, 2017
Notes: 1

## Slide 2
Importance of User Authentication
At almost every corner of our daily lives
Smart access systems require the authentication process to play a broader role
Apartment Buildings
Private Devices
Secret Documents
Vehicle Doors
Smart Homes

## Slide 3
Smart Access Systems: Existing Authentication Techniques
Involve costly equipment, complex hardware installation and diverse maintenance needs
Intercom
Camera
Card
Fingerprint
The deployment of smart access systems will reach the market value of $9.8 billion by 2022

## Slide 4
Token devices (e.g., smart glove or pen) on touch screen
Ultra-thin sensing pad can be deployed in automobiles
Existing techniques require that the touched surface possesses electric conductivity, or specialized sensing pad
Trend of User Authentication
Capacitive Touch Authentication
Low-cost low-power tangible user interfaces

## Slide 5
Can we push the limits of the touched surface? - support authentication on any surface?
<Mission Impossible 5>
Convert any solid surface to an authentication surface for general user authentication!

## Slide 6
Finger-input authentication via vibration in smart access systems
  Support any solid surface
Capture intrinsic human behavioral and physiological characteristics
  Extract unique vibration features from finger-touch
Contributions

## Slide 7
Contributions
Support three types of secrets
Correctly recognize the passcode entered by the legitimate users
Prototype
Notes: Turn in to

## Slide 8
Apply Physical Vibration
Actively excite a surface resulting in the shockwave;
Measure the change of the vibration signals to sense touches.
Vibration Motor
Vibration Receiver
Basic Idea of Touch Sensing

## Slide 9
Can we utilize such sensing technique to authenticate users and reject attackers?

## Slide 10
  Unique features are embedded in a user’s finger input
  Fingertip size and structure
  Locations of touching, contacting area, touching force, etc.
Finger touch: behavioral and physiological characteristics
Insights for Authentication

## Slide 11
Key Observations
  Discriminate different touching locations and touching fingers
  Strongly influenced by unique human behavior/physiological traits
Same User, Different Location
Different User, Same Location
Pearson correlation (Similarity Comparison)
Observations

## Slide 12
Blind Attack
    An adversary randomly touches
Credential-aware Attack
      An adversary has the prior knowledge of the legitimate user’s credentials, but does not possess the knowledge of the VibWrite setting details
Knowledgeable Observer Attack
  Attackers know the passcodes & how the legitimate users inputs them
Side-channel Attack
  Placing hidden vibration receiver & nearby microphones
Attack Models

## Slide 13
System Overview (VibWrite)
Notes: Before it, add attack.

## Slide 14
  Repeated chirp vibration signals to linearly sweep frequency from 16kHz to 22kHz
  Avoid distracting users
  Frequency is much higher than the frequency range of other unrelated noises
Vibration Signal Design

## Slide 15
  Vibration Signal Synchronization
  Using cross-correlation between the PN sequence of the received vibration signal and the known generated PN sequence.
  Clock Drift Effect Mitigation
    Sampling rate may be not a fixed value over time due to imperfect clock
    Estimate the sampling rate offset during a short calibration phase
Vibration Signal Calibration

## Slide 16
Analyze the received vibration signals in the frequency domain using a 200ms sliding window (16~22kHz)
  Transmitted chirp vibration signal has fundamental frequencies 1/T (100Hz, T=10ms)
  Spectral points are the most sensitive to the minute changes caused by finger touching
  Spectral points at every 100Hz interval
Distinguishable spectral points when a finger presses 4 different locations
Spectral Point-based Feature Extraction

## Slide 17
Mel-frequency cepstral coefficient (MFCC)
  Short-term power spectrum of acoustic signals
  Can well capture any changes associated with the vibrating surface
Example of the extracted MFCC features
MFCC-based Feature Extraction

## Slide 18
Deriving Grid Point Index Traces
  SVM-based Grid Point Classifier
Grid Point Index Filtering
  Segments that have consecutive same grid point indices
PIN Sequence/Lock-pattern Derivation
  Remove the finger-press segments with shorter time duration
Passed
Passed
Attacker:Rejected
1
2
6
7
1
2
5
9
1
5
4
8
Authentication Using PIN Numbers & Lock Patterns

## Slide 19
Gesture Segmentation
  Feature differences (received vibration signals vs. empty surface profile)
Distance Calculation of Feature Sequence
  Dynamic Time Warping (DTW)
  Earth Mover’s Distance (EMD)
Authentication Using Gesture

## Slide 20
3*3 square-shaped grid in a typical office environment
  Wooden table
  Door panel
Prototyping
  Linear Resonant Actuator (LRA) based motor
  A piezoelectric sensor
15 participants were involved
  450 genuine input passcodes for each motor/receiver placement
Experimental Setup & Prototyping
Notes: Add a pic of sensor

## Slide 21
Over 95% verification accuracy of recognizing each PIN digit and recognizing the complete PIN sequence reaches 90%
Average verification accuracy of the lock pattern reaches 95% with two trials
Verifying Legitimate Users

## Slide 22
Attackers can break PIN sequences with 2% and lock patterns with 5% success rates
Knowledgeable Observer Attacks

## Slide 23
Proposed VibWrite, the low-cost low-power tangible user authentication beyond touch screens on any solid surface
Demonstrated that vibration can capture unique human physiological and behavioral characteristics presenting through finger-input
Implemented a prototype using a single pair of vibration motor and receiver
Demonstrated the robustness of the system under various attacks on different surfaces
Conclusion

## Slide 24
Accuracy, and Further Improvement
  Deploying multiple sensor pairs
  Refining the hardware
  Improving the authentication algorithms
Coping with Additional Physical Attacks
  Denial-of-service (DoS) attack
System Maintenance
  Dealing with various environmental factors
Limitations and Future Work
Notes: This is just an academic prototype

## Slide 25
Jian Liu
jianliu@winlab.rutgers.edu http://www.winlab.rutgers.edu/~jianliu/
DAISY Data Analysis and Information SecuritY Lab